## Slide 1: Practical investigation of Rayleigh fading model in URC conditions
Andreas Vembe Jäger Mads Røgeskov Gotthardsen Markos Vourvachis Thomas Kær Juel Jørgensen

## Slide 2: Introduction
Fading and multipath outages
Ultra Reliable Low Latency Communication(URLLC) 5G
Cable replacement
Low latency means low error correction coding
Future applications

## Slide 3: Introduction
Rayleigh fading channels
“Log-Log linear”
Fading gain of 10e-5 / -50dB
Extrapolated models

## Slide 4: Problem statement
Design a measurement system that can handle very deep fades and a statistical method to process the data and compare to existing Rayleigh model used in URLLC channels.
Statistically sufficient amount of samples.
Sufficient Dynamic Range to see the deep fades.

## Slide 5: Statistical Aspect
Estimation of sample pool.
Normal approximation of the Binomial proportion.
Confidence level and interval
The goal was 90% and ±1dB respectivly
Important sampling
Bootstrap method
Simulation of bootstrap method

## Slide 6: Wireless Channel
Multipath fading
  Large scale
  Small scale
    Flat Fading
    Selective Fading
Diversity
  Temporal
  Spatial
  Frequency
Diversity Combining
Rayleigh Fading(Non-Line Of Sight , Urban fading model)

## Slide 7: Doppler Bandwidth
Relative velocity between Tx-Rx

## Slide 8: Wireless Channel Characteristics
Multipath fading channels are described by 2 domains(Temporal-Spatial).
Utilization of both domains for a large sample pool.
Domain Transformation with FFT.
4 representations(insert picture here)

## Slide 9: WSSUS
WSS – Temporal domain
US – Spatial domain
One parameter per domain
Independent domains

## Slide 10: Space Correlation Function
FFT of Doppler spectrum
Assuming Rayleigh and Jakes bathtub.
  Zero order bessel function
Uncorrelated samples 0.38λ

## Slide 11: Frequency Correlation Function
FFT of Power Delay Profile(PDP)
Assuming exponential decay PDP
Small environment more Δf is needed
Approximation of coherence bandwidth
RMS delay spread inversely proportioned to coherence bandwidth

## Slide 12: Receiver Structure
(insert structure photo here)
Explain each part of the structure
Receiver is influenced by :
  Gain
  Distortion
  Noise
Correction with Network Analyzer
Calibration

## Slide 13: Dynamic Range
Sensitivity of the receiver to Max signal strength
Sensitivity lowest signal that meets the receiver’s criteria
In NA sensitivity=noise floor
Tradeoff between Narrowband-Wideband sample acquisition
Digital signal processing – averaging

## Slide 14: SNR Margin Estimation
Distinguish noise from deep fades
Rician distribution
  LOS connection
  K-factor is LOS signal to scattered signals
K-factor to SNR connection
For 90% confidence level and ± 1dB interval SNR margin is 14dB

## Slide 15: Measurement Setup
(insert picture of designed room)

## Slide 16: Equipment
Keysight 4-port Network Analyzer
Dynamic Range 131dB and Frequency Range 10MHz to 67GHz
Simple Calibration
3 RX cables(10m) and 1 TX cable(4m) with cable loss 0.5dB/m
RX omnidirectional antenna array fc 5GHz and 0.4λ spacing
Directional TX antenna 12dBi Gain and fc 5GHz
(insert figure 5.6)

## Slide 17: Measurement of Coherence Bandwidth
PDP measurement
20 different positions in the measurement area
(insert figure 4.1)
RMS delay spread 14ns = 71.5MHz
New measurement with Δf 5MHz
Autocorrelation function to determine the Frequency Correlation
(insert figure 7.2)
Correlation < 0.3 with Bc 25MHz

## Slide 18: Fading Measurements-Results
162 walks for total combined length of 810 meters
Total 4,184,460 samples

## Slide 19: Data Processing
Stationarity WSSUS criteria
Data structure Frequency , Antenna and Space/walk
Frequency stationarity(insert figure 8.2)
Spatial stationarity
Visualization of the space data(insert figures 8.3)
Main lobe reflection – not stationary
Moving average required (insert figures for 8.4)

## Slide 20: WSS and US proof
Check if auto-correlation depends only on the time lag
Sample mean and variance were found for both frequency and space
For each element the cross-covariance matrix is found
The variance across the diagonal elements is close to zero and depends only on time lag
A higher diagonal variance in the spatial domain indicates a dominant component in the signal
Still work under the assumption that both domains are stationary

## Slide 21: Verification of the Phase
Uniformly distributed (insert picture)

## Slide 22: Frequency , Antenna and space correlation
Correlation < 0.3 is considered uncorrelated.
(insert figure 8.7)
Antenna’s and frequency’s samples are uncorrelated
Space samples are too correlated with correlation of 0.45
Cause of this could be slow movement or the stationarity issue in space
The way to fix it was to remove samples from the sample pool
Every other sample was removed giving a correlation of 0.165

## Slide 23: Results
Because of the lower sample size of 2,902,230 the confidence interval is increased to ±1.33dB
10,000 bootstraps (insert figure 8.9)
-51.59dB fading gain with ±1.37dB interval

## Slide 24: Results
Relative error of the measurements compared to the Rayleigh fading model.
(insert figure 8.10)

## Slide 25: Diversity Combining
Looking at different diversity orders
Combining frequency and antenna diversity
(insert picture with different diversity orders for frequency)
(insert picture for combined )
Diminishing returns of diversity order > 4

## Slide 26: Uncertainties