## Slide 1: Practical investigation of Rayleigh fading model in URC conditions
Andreas Vembe Jäger Mads Røgeskov Gotthardsen Markos Vourvachis Thomas Kær Juel Jørgensen
WCS8 Gr. 850

## Slide 2: Agenda
Introduction
Statistical Aspect
Wireless Channel
WSSUS
Correlation
Dynamic Range
Measurement Setup
Data Processing
Results
Diversity Combining
Uncertainties
Further Work
Notes: Add picture for 5G

## Slide 3: Introduction
Notes: Fading and multipath outages
Ultra Reliable Low Latency Communication(URLLC) 5G
Cable replacement
Low latency means low error correction coding
Future applications

## Slide 4: Introduction
Notes: Rayleigh fading channels
“Log-Log linear”
Fading gain of 10e-5 / -50dB
Extrapolated models

## Slide 5: Problem statement
Design a measurement system that can handle very deep fades and a statistical method to process the data and compare to existing Rayleigh model used in URLLC channels.

## Slide 6: Wireless Channel
Notes: Multipath fading
  Large scale
  Small scale
    Flat Fading
    Selective Fading

## Slide 7: Wireless Channel
Notes: Rayleigh Fading(Non-Line Of Sight , Urban fading model)

## Slide 8: Statistical Aspect
Notes: Estimation of sample pool.
Normal approximation of the Binomial proportion.
Confidence level and interval
The goal was 90% and ±1dB respectivly
Important sampling
Bootstrap method
Simulation of bootstrap method

## Slide 9: Statistical Aspect
Notes: Estimation of sample pool.
Normal approximation of the Binomial proportion.
Confidence level and interval
The goal was 90% and ±1dB respectivly
Important sampling
Bootstrap method
Simulation of bootstrap method

## Slide 10: Wireless Channel
Temporal domain
Spatial domain

## Slide 11: WSSUS
WSS – Temporal domain
US – Spatial domain
One parameter per domain
Independent domains

## Slide 12: Space Correlation Function
FFT of Doppler spectrum
Assuming Rayleigh and Jakes bathtub.
  Zero order bessel function
Uncorrelated samples 0.38λ

## Slide 13: Frequency Correlation Function
FFT of Power Delay Profile(PDP)
Assuming exponential decay PDP
Small environment more Δf is needed
Approximation of coherence bandwidth
RMS delay spread inversely proportioned to coherence bandwidth

## Slide 14: Receiver Structure
The basic receiver’s structure.
Receiver is influenced by :
  Gain
  Distortion
  Noise
Noise is the dominant factor.
Calibration for distortion

## Slide 15: Dynamic Range
Sensitivity of the receiver to Max signal strength
Sensitivity lowest signal that meets the receiver’s criteria
In NA sensitivity=noise floor
Tradeoff between Narrowband-Wideband sample acquisition
Digital signal processing – averaging

## Slide 16: SNR Margin Estimation
Distinguish noise from deep fades
Rician distribution
  LOS connection
  K-factor is LOS signal to scattered signals
K-factor to SNR connection
For 90% confidence level and ± 1dB interval SNR margin is 14dB

## Slide 17: Measurement Setup
The measurements were contacted in the blue shaded space while The antenna position is circled with red.

## Slide 18: Equipment
Keysight 4-port Network Analyzer
Normalization of signal
RX omnidirectional antenna array fc 5GHz and 0.4λ spacing
Directional TX antenna 12dBi Gain and fc 5GHz

## Slide 19
Measurement of Coherence Bandwidth
PDP measurement
20 different positions in the measurement area
RMS delay spread 14ns = 71.5MHz
New measurement with Δf 5MHz
Autocorrelation function to determine the Frequency Correlation
Correlation < 0.3 with Bc 25MHz

## Slide 20
Fading Measurements-Results
162 walks for total combined length of 810 meters
41 frequency, 3 antennas and 34,020 space samples
Total 4,184,460 samples

## Slide 21
Data Processing
WSS stationarity criteria
Pathloss and Antenna gain
Normailze the data

## Slide 22
Data Processing
US stationarity criteria
Main lobe reflection – not stationary
Moving average required

## Slide 23
WSS and US proof
Check if auto-correlation depends only on the time lag
Sample mean and variance were found for both frequency and space
For each element the cross-covariance matrix is found
The variance across the diagonal elements is close to zero and depends only on time lag
A higher diagonal variance in the spatial domain indicates a dominant component in the signal
Still work under the assumption that both domains are stationary

## Slide 24
Frequency, Antenna and space correlation
Correlation < 0.3 is considered uncorrelated.
Antenna’s and frequency’s samples are uncorrelated
Space samples are too correlated with correlation of 0.45
Cause of this could be slow movement or the stationarity issue in space
The way to fix it was to remove samples from the sample pool
Every other sample was removed giving a correlation of 0.165

## Slide 25
Results
Because of the lower sample size of 2,092,230 the confidence interval is increased.
10,000 bootstraps was used to find the end interval
-51.59dB fading gain with ±1.37dB interval of 90% confidence level

## Slide 26
Results
Relative error of the measurements compared to the Rayleigh fading model.

## Slide 27: New Results

## Slide 28: Diversity Combining

## Slide 29: Uncertainties
WSSUS
  Distance
  Human error
  Wide bandwidth
Phase correlation

## Slide 30: Further Work
Using diversity to minimize needed SNR level
Using four antennas instead of three
Moving faster

## Slide 31: Summary
Introduction
Statistical Aspect
Wireless Channel
WSSUS
Correlation
Dynamic Range
Measurement Setup
Data Processing
Results
Diversity Combining
Uncertainties
Further Work