## Slide 1: Practical investigation of Rayleigh fading model in URC conditions
Andreas Vembe Jäger Mads Røgeskov Gotthardsen Markos Vourvachis Thomas Kær Juel Jørgensen

## Slide 2: Agenda
Introduction
Statistical Aspect
Wireless Channel
WSSUS
Correlation
Dynamic Range
Measurement Setup
Data Processing
Results
Diversity Combining
Uncertainties
Further Work
Notes: Add picture for 5G

## Slide 3: Introduction
Notes: Fading and multipath outages
Ultra Reliable Low Latency Communication(URLLC) 5G
Cable replacement
Low latency means low error correction coding
Future applications

## Slide 4: Introduction
Notes: Rayleigh fading channels
“Log-Log linear”
Fading gain of 10e-5 / -50dB
Extrapolated models

## Slide 5: Problem statement
Design a measurement system that can handle very deep fades and a statistical method to process the data and compare to existing Rayleigh model used in URLLC channels.

## Slide 6: Statistical Aspect
Notes: Estimation of sample pool.
Normal approximation of the Binomial proportion.
Confidence level and interval
The goal was 90% and ±1dB respectivly
Important sampling
Bootstrap method
Simulation of bootstrap method

## Slide 7: Statistical Aspect
Notes: Estimation of sample pool.
Normal approximation of the Binomial proportion.
Confidence level and interval
The goal was 90% and ±1dB respectivly
Important sampling
Bootstrap method
Simulation of bootstrap method

## Slide 8: Wireless Channel
Notes: Multipath fading
  Large scale
  Small scale
    Flat Fading
    Selective Fading

## Slide 9: Wireless Channel
Notes: Rayleigh Fading(Non-Line Of Sight , Urban fading model)

## Slide 10: Wireless Channel
Temporal diversity
Spatial diversity

## Slide 11: Doppler Bandwidth

## Slide 12: Wireless Channel Characteristics
Notes: Multipath fading channels are described by 2 domains(Temporal-Spatial).
Utilization of both domains for a large sample pool.
Domain Transformation with FFT.
4 representations(insert picture here)

## Slide 13: WSSUS
WSS – Temporal domain
US – Spatial domain
One parameter per domain
Independent domains

## Slide 14: Space Correlation Function
FFT of Doppler spectrum
Assuming Rayleigh and Jakes bathtub.
  Zero order bessel function
Uncorrelated samples 0.38λ

## Slide 15: Frequency Correlation Function
FFT of Power Delay Profile(PDP)
Assuming exponential decay PDP
Small environment more Δf is needed
Approximation of coherence bandwidth
RMS delay spread inversely proportioned to coherence bandwidth

## Slide 16: Receiver Structure
The basic receiver’s structure.
Receiver is influenced by :
  Gain
  Distortion
  Noise
Noise is the dominant factor.
Calibration for distortion

## Slide 17: Dynamic Range
Sensitivity of the receiver to Max signal strength
Sensitivity lowest signal that meets the receiver’s criteria
In NA sensitivity=noise floor
Tradeoff between Narrowband-Wideband sample acquisition
Digital signal processing – averaging

## Slide 18: SNR Margin Estimation
Distinguish noise from deep fades
Rician distribution
  LOS connection
  K-factor is LOS signal to scattered signals
K-factor to SNR connection
For 90% confidence level and ± 1dB interval SNR margin is 14dB

## Slide 19: Measurement Setup
The measurements were contacted in the blue shaded space while The antenna position is circled with red.

## Slide 20: Equipment
Keysight 4-port Network Analyzer
Dynamic Range 131dB and Frequency Range 10MHz to 67GHz
Simple Calibration
3 RX cables(10m) and 1 TX cable(4m) with cable loss 0.5dB/m
RX omnidirectional antenna array fc 5GHz and 0.4λ spacing
Directional TX antenna 12dBi Gain and fc 5GHz

## Slide 21
Measurement of Coherence Bandwidth
PDP measurement
20 different positions in the measurement area
RMS delay spread 14ns = 71.5MHz
New measurement with Δf 5MHz
Autocorrelation function to determine the Frequency Correlation
Correlation < 0.3 with Bc 25MHz

## Slide 22
Fading Measurements-Results
162 walks for total combined length of 810 meters
Total 4,184,460 samples

## Slide 23
Data Processing
Stationarity WSSUS criteria
Data structure Frequency , Antenna and Space/walk
Frqunecy stationarity
Pathloss and Antenna gain
Normailze the data

## Slide 24
Data Processing
Stationarity WSSUS criteria
Data structure Frequency , Antenna and Space/walk
Spatial stationnary
Main lobe reflection – not stationary
Moving average required

## Slide 25
WSS and US proof
Check if auto-correlation depends only on the time lag
Sample mean and variance were found for both frequency and space
For each element the cross-covariance matrix is found
The variance across the diagonal elements is close to zero and depends only on time lag
A higher diagonal variance in the spatial domain indicates a dominant component in the signal
Still work under the assumption that both domains are stationary

## Slide 26
Frequency , Antenna and space correlation
Correlation < 0.3 is considered uncorrelated.
Antenna’s and frequency’s samples are uncorrelated
Space samples are too correlated with correlation of 0.45
Cause of this could be slow movement or the stationarity issue in space
The way to fix it was to remove samples from the sample pool
Every other sample was removed giving a correlation of 0.165

## Slide 27
Results
Because of the lower sample size of 2,092,230 the confidence interval is increased.
10,000 bootstraps was used to find the end interval
-51.59dB fading gain with ±1.37dB interval of 90% confidence level

## Slide 28
Results
Relative error of the measurements compared to the Rayleigh fading model.

## Slide 29: New Results

## Slide 30: Diversity Combining

## Slide 31: Uncertainties
WSSUS
  Distance
  Human error
  Wide bandwidth
Phase correlation

## Slide 32: Further Work
Using diversity to minimize needed SNR level
Using four antennas instead of three
Moving faster

## Slide 33: Summary
Introduction
Statistical Aspect
Wireless Channel
WSSUS
Correlation
Dynamic Range
Measurement Setup
Data Processing
Results
Diversity Combining
Uncertainties
Further Work